## Slide 1: Recent Development on IN3D-ACC July 22, 2014
Lixiang (Eric) Luo, Jack Edwards, Hong Luo
Department of Mechanical and Aerospace Engineering
Frank Mueller Department of Computer Science
North Carolina State University

## Slide 2: Collaboration
Collaboration with F. Muller’s group (NCSU CS)
  Invaluable cluster and software support by Muler’s group.
  Technical challenges on OpenACC and CUDA are actively discussed.
Collaboration with RDGFLO3D (NCSU MAE)
  Repositories of codes are set up for easy access.
  Common algorithms on implicit methods are shared, reducing code development effort.
  Y. Xia, L. Luo, H. Luo, J. Lou, J. Edwards, F. Mueller, “On the Multi-GPU Computing of a Reconstructed Discontinuous Galerkin Method for Compressible Flows on 3D Hybrid Grids,” AIAA Aviation 2014, Georgia
Incorporation of GPU-aware functionalities of MVAPICH2 (VT CS)
  With the support on MVAPICH2 from Hao Wang, INCOMP3D is able to conduct efficient data transfers across GPUs on different cluster nodes.
  Portability of the data transfer codes is greatly improved.
  H. Wang, S. Potluri, D. Bureddy, C. Rosales, D. K. Panda, "GPU-Aware MPI on RDMA-Enabled Clusters: Design, Implementation and Evaluation," IEEE Transactions on Parallel and Distributed Systems, vol. 99, PrePrints, 2014.
Advanced wavefront scheme for the implicit solvers (VT CS)
  An advanced synchronization scheme pioneered by Feng’s group (VT CS) is being studied.
  S. Xiao, W. Feng, “Inter-Block GPU Communication via Fast Barrier Synchronization,” 24th IEEE International Parallel and Distributed Processing Symposium, Atlanta, Georgia, April 2010.

## Slide 3: Publication (first author only)
L. Luo, J. Edwards, H. Luo, F. Mueller, “GPU Port of A Parallel Incompressible Navier-Stokes Solver based on OpenACC and MVAPICH2,” AIAA Aviation 2014, Atlanta, Georgia, June 2014.
L. Luo, J. Edwards, H. Luo, F. Mueller, "Performance Assessment of A Multi-block Incompressible Navier-Stokes Solver using Directive-based GPU Programming in a Cluster Environment." AIAA SciTech 2014, Baltimore, Maryland, January 2014.

## Slide 4: Upcoming Tasks
Accuracy study and optimization of 2-stage BILU(0)
  Storage of factorized is different from the original algorithm.
  Triangle substitution needs modification.
  Solver accuracy may be slightly different from the original codes.
Scheduling multiple blocks on one GPU – rehashing
  Balance must be found between “size of blocks” vs. “number of blocks”.
Improvement on MPI
  Recently available hardware GPU RDMA may improve MPI efficiency.
  General data exchange libraries can be adopted.
Atomic operations instead of coloring schemes
  Atomic operations are now available in PGI’s latest compilers supporting OpenACC 2.0.
Two-level synchronization in wavefront scheme
Further optimizations of other kernels (flux, BC, LHS)

## Slide 5: Review of Previous Report: AIAA Aviation 2014
An implicit solver is fully operational
Performance tests show an overall speedup of 3x
Most computation-intensive tasks reach 4x speedup
MPI data transfer is relatively slow
The naïve implementation of BILU(0) has least speedup (~2.3x)
Test case: 700K grid, 100 steps
Chart: 
| 6x c2050 | 6x CPU
AFILL | 17 | 75
TSD | 11 | 41
ILU(0) | 22 | 50
Triangle Solve | 13 | 55
Flux | 14 | 64
Correction | 7 | 10
Dada Packing | 1.1 | 4
MPI Transfer | 26 | 28
Notes: So we then carryout out a performance assessment of the ported coded. ..

## Slide 6: Brief Review of BILU(0)
A first-order fully implicit time marching leads to a block-sparse linear system
where the LHS matrix appears in the following form
 | An |  |  | Bn |  | Cn | Dn | En |  | Fn |  |  | Gn | 
i, j+1, k
i, j-1, k
i+1, j, k
i-1, j, k
i, j, k+1
i, j, k-1
Notes: Porting the implicit schemes onto GPU prove to be the most challenging task of this research. All our previous issues I just talked can more or less be seen as technical issues. On the other hand, getting implicit scheme to work is essentially a mathematical challenge that must be address from its root. I believe many people working with GPU already found that porting implicit schemes to be rather difficult. The crux of the difficulty comes from the inevitable step: solving a linear system. There is are highly parallel iterative solvers out there but their performance is far from satisfying. To get better performance some kind of sequential process must be involved. The reason is simple, the effectiveness of implicit schemes comes from the internal data dependency, which is the biggest enemy of GPGPU. Let me return to our attempt to address this challenge.

## Slide 7: Block-sparse Linear System
The 7 blocks are the results of the 7-point stencil used in our structured FVM method.
Each block is 6x6, due to the 6 unknowns: , where is turbulence kinetic energy and is turbulence frequency.
ILU(0): incomplete LU decomposition with zero fill-in
Block ILU (BILU) is a counterpart of point ILU for block-sparse linear systems. Instead of scalars, BILU(0) operates on identical-sized submatrices.

## Slide 8: The BILU(0) Algorithm
When the matrix is generated by a structured grid with 7-point stencil, BILU(0) takes a simple recursive form:
The BILU(0) factorization allows estimated solution by two triangle sweeps:
where is the complete block-diagonal matrix consists of all .

## Slide 9: Comparison of Per-thread Timing
 | BILU(0) | Triangle Solver
Total runtime | 0.2087 | 0.03584
Total threads | 189679 | 
Actual per-thread runtime | 1.1 μ s | 0.19 μ s
Optimal per-thread runtime | 1.0 μ s | 0.165 μ s
Loss | 10% | 14%
More than 70% of the hyperplanes run at (near) optimal speed
To further quantify the performance loss due to insufficient load, a comparison is made:
Conclusion: performance loss due to insufficient load is not the dominant factor.
Notes: However, we also need to notice that more than… If every point in the point runs at optimal speed, how much can the overall performance improve?

## Slide 10: BILU(0) is Actually Heavily Memory-bound
Each thread needs to access 7 6x6 submatrices and 3 6x6 temporary matrices
  Only one submatrix may overlap with adjacent thread
Assume each thread need to access 9 6x6 matrices, a CUDA wrap (32 threads) would need data –more than CUDA L1 data cache.
The primary cause of the poor performance of BILU(0) is the extremely low data coagulation.
  The apparent data throughput is only: 83KB/32/1.1s=2.4GB/s
Performance is further worsened by cache overflow due to large amount of data to access

## Slide 11: An Attempt to Improve BILU(0)
The key of improving BILU(0) performance is granularity reduction
  Less memory access per kernel, thus less memory-bound
  Less performance loss due to insufficient load
Without changing the overall algorithm, the BILU(0) recursion can be reorganized as a two stage process:
Carry out the inversion of all on the previous hypaerplane.
Carry out the block matrix multiplication in a per-element fashion in the current hyperplane.

## Slide 12: Pseudocode
  Do ipl = ii+jj+kk,6,-1 ! loop over all hyperplanes
  Do ie = 1, ipoint(ipl+1) ! D inversion on the previous hyperplane
  …
  End Do
  Do ip = 0, ipoint(ipl)*36-1 ! per-element matrix multiplication
  <carry out >
  End Do
  Do ip = 0, ipoint(ipl)*36-1 ! per-element matrix multiplication
  <carry out >
  End Do
  …
  <carry out similar matrix multiplications for and >
  End Do

## Slide 13: Current Progress
BILU(0) factorization has been implemented with the new 2-stage algorithm in OpenACC
The block matrix inversion alone reaches 8x speedup over an equivalent CPU version
The matrix multiplication alone reaches over 30x speedup over an equivalent CPU version
Overall speedup is 7.1x for BILU(0). For a test block 50x50x80:
CPU, original, wavefront, unrolled: 0.49s
GPU, 2-stage, wavefront, unrolled inversion: 0.069s
CPU, 2-stage, wavefront, unrolled inversion: 1.5s

## Slide 14: Kernel Runtimes
Matrix multiplication is very efficient
Matrix inversion is more affected by insufficient load due to coarse granularity