## Slide 1: Development of a Portable, GPU-Accelerated Discontinuous Galerkin CFD Code for Compressible Flows on Unstructured Hybrid Grids
Jialin Lou, Xiaodong Liu, Lixiang Luo, Hong Luo, and Jack Edwards
Department of Mechanical and Aerospace Engineering
North Carolina State University
and
Frank Mueller, and Saransh Gupta
Department of Computer Science
North Carolina State University
AFOSR BRI
Co-Design of Hardware/Software for Predicting UAV Aerodynamics
Presented by Xiaodong Liu, Ph.D. Student ,
July 20-21, 2015

## Slide 2: Outline
A brief overview
Motivation and objective
Governing equations of fluid dynamics
Discontinuous Galerkin formulation
Development of RDGFLO solver
Application
Concluding remarks
Future work
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 3: GPU Computing in CFD – Overview
GPGPU
General-purpose computing on graphics processing units The utilization of GPU, which typically handles computation only for computer graphics, to perform computation in applications traditionally handled by CPU.
Why?
The great potential and scalability of GPGPU for CFD applications!
How?
Offload the computing-intensive portion from the host CPUs to the GPU devices.
Programming models
OpenCL: the currently dominant open GPGPU programming language NVIDIA’s CUDA: the dominant proprietary framework OpenACC: a collection of directives designed to simplify parallel programming
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics
Notes: Not new concept. It’s roughly clear to everyone in scientific computing why you want to it and how you can do it. But maybe a lot of people do not know much what specific method to try.

## Slide 4: GPU Computing in CFD – Overview
A variety of applications (selected)
For the finite difference method (FDM) E. Elsen, P. LeGresley, and E. Darve. Large Calculation of the Flow over a Hypersonic Vehicle Using a GPU. J. Comput. Phys., 227(24):10148–10161, 2008. For the finite volume method (FVM) A. Corrigan, F. Camelli, R. Löhner, and J. Wallin. Running Unstructured Grid-based CFD Solvers on Modern Graphics Hardware. Int. J. Numer. Methods Fluids, 66(2):221–229, 2011. For the spectral difference method (SDM) B. Zimmerman, Z. Wang, and M. Visbal. High-Order Spectral Difference: Verification and Acceleration Using GPU Computing. AIAA Paper, 2013-2491, 2013. For the discontinuous Galerkin method (DGM) A. Klöckner, T. Warburton, J. Bridge, and J. S. Hesthaven Nodal Discontinuous Galerkin Methods on Graphics Processors. J. Comput. Phys., 228(21):7863–7882, 2009.
Observation: most GPU-related CFD solvers are based on CUDA
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 5: Motivation & Objectives
Motivation
Tap the power of GPU parallel computing for the aerodynamic design of Unmanned Aerial Vehicle (UAV) with CFD toolkits
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics
MQ-1 Predator UAV (Source: grabcad.com CAD by Chao Wey)

## Slide 6: Motivation & Objectives
Objectives
A portable, efficient and ultimately competitive GPU parallelization strategy for extensible and sustainable high-fidelity CFD code development
An unavoidable debate – CUDA, OpenCL or OpenACC?
It really depends on your needs, e.g., for us, cross-platform portability Support from a wide range of compiler and accelerator vendors C/C++ and Fortran Best performance Less fine-tuning effort, especially for a legacy code package Available computing resource
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 7: GPU-Computing Framework
Desirable features of the resulting CFD code
Multi-compiler compatibility GNU Fortran compiler Intel Fortran compiler PGI Accelerator Fortran compiler (with OpenACC support) CAPS Fortran compiler (with OpenACC support) Cross-platform portability Intel CPUs AMD CPUs / APUs (with potential OpenACC support in 2014) NVIDIA CUDA-enabled GPUs (with OpenACC support) Extensible and sustainable programming schemes Competitive performance
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics
Notes: In a practical sense, the current OpenACC-based code does not enjoy a wide range of portability.

## Slide 8: Legacy CFD Package
RDGFLO – a baseline code for OpenACC-based GPU parallelization
A Reconstructed Discontinuous Galerkin finite element FLOw solver High-order solution of compressible flows on 3-D hybrid grids Explicit / implicit solution schemes Domain-partition based MPI parallel computing
Gallery
ONERA M6 wing
wing/pylon/finned-store configuration
Boeing 747 aircraft
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 9: Governing Equations of Fluid Dynamics
The Navier-Stokes equations for unsteady compressible flows
where the summation convention is used. The conservative variable vector U, advective flux vector F, and viscous flux G are defined by
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 10: Governing Equations of Fluid Dynamics
The Navier-Stokes equations for unsteady compressible flows (cont.)
The pressure p can be computed from the equation of state (EOS) which is valid for perfect gas. The ratio of specific heats γ is assumed to be constant and equal to 1.4. The viscous stress tensor τij and heat flux vector qj are given by where T is the temperature of the fluid, Pr the laminar Prandtl number, which is 0.7 for air. μ represents the molecular viscosity, which can be determined through the Sutherlands law where μ0 is the viscosity at the reference temperature T0 and S = 110K.
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 11: Discontinuous Galerkin Method
Weak formulation of the governing equations
where Bi(x) is the basis function of polynomials of degree p, and N is the dimension of the polynomial space p. The Taylor-basis discontinuous Galerkin (DG(p)) solution in each element For example, the underlying piecewise linear polynomial DG(P1) solution where (xc, yc, zc) is the coordinate of the element center.
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 12: Discontinuous Galerkin Method
Hierarchical WENO reconstruction
A quadratic polynomial DG(P2) solution is obtained via a hierarchical WENO reconstruction approach in each element Least-squares reconstruction to obtain an initial quadratic solution WENO reconstruction for the second derivatives to maintain linear stability WENO reconstruction for the first derivatives to maintain nonlinear stability Reference articles H. Luo, Y. Xia, S. Li, and R. Nourgaliev. A Hermite WENO Reconstruction-Based Discontinuous Galerkin Method for the Euler Equations on Tetrahedral grids. J. Comput. Phys. 231(16):5489–5503, 2012. H. Luo, Y. Xia, S. Spiegel, R. Nourgaliev, and Z. Jiang. A Reconstructed Discontinuous Galerkin Method Based on a Hierarchical WENO Reconstruction for Compressible Flows on Tetrahedral Grids. J. Comput. Phys. 236:477–492, 2013.
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 13: Discontinuous Galerkin Method
Semi-discrete form
A system of ordinary differential equations (ODEs) in time where M is the mass matrix and R is the residual vector. Three-stage TVD Runge-Kutta (TVDRK3) time stepping
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 14: Design of OpenACC Parallel Regions
Example: a readily vectorizable region | 
Domain integral: loop over mesh elements Ωe | 
OpenMP version !$omp parallel !$omp do do ie = 1, Nelem do ig = 1, Ngp !... contribution to this element rhsel(:, :, ie) = rhsel(:, :, ie) + flux enddo enddo !$omp end parallel | OpenACC version !$acc parallel !$acc loop do ie = 1, Nelem do ig = 1, Ngp !... contribution to this element rhsel(:, :, ie) = rhsel(:, :, ie) + flux enddo enddo !$acc end parallel
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 15: Design of OpenACC Parallel Regions
Example: a region that is not readily vectorizable | 
Face integral: loop over mesh faces Τe | 
OpenMP version !$omp parallel !$omp do do ifa = Njfac+1, Nafac do ig = 1, Ngp !... contribution to the face-left element rhsel(:, :, iel) = rhsel(:, :, iel) - flux !... contribution to the face-right element rhsel(:, :, ier) = rhsel(:, :, ier) + flux enddo enddo !$omp end parallel | OpenACC version !$acc parallel !$acc do do ifa = Njfac+1, Nafac do ig = 1, Ngp !... contribution to the face-left element rhsel(:, :, iel) = rhsel(:, :, iel) - flux !... contribution to the face-right element rhsel(:, :, ier) = rhsel(:, :, ier) + flux enddo enddo !$acc end parallel
“race condition” – multiple writes to the same elemental residual vector!
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 16: Design of OpenACC Parallel Regions
A common method for avoiding “race condition” in face integral
Perform face integral at the element level All the computing is implemented as loops over mesh elements Overheads Lead to redundant computation of face integrals (doubled!) Require an additional element-face connectivity array Reference articles on unstructured DG/FV methods (with CUDA) A. Corrigan et al. Running Unstructured Grid-based CFD Solvers on Modern Graphics Hardware. Int. J. Numer. Methods Fluids, 66(2):221–229, 2011. Tristan Cabel and Stephane Lanteri. Discontinuous Galerkin Time-Domain Solver on GPU Based Systems. Plafrim meeting, May 31, 2011
This design approach requires a major rebuild in code structures!
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics
Notes: This “element based” loop strategy is still a very fast method on GPU devices, if you read the referred papers

## Slide 17: Design of OpenACC Parallel Regions
An alternative approach to avoiding “race condition” in face integral
Face renumbering (coloring method) renumber the faces and split them into several groups. Any two faces that share a common cell do not reside in the same group. The original face loops are nested in a sequential loop over groups.
An example of “face renumbering & grouping” |  |  |  |  |  |  |  |  |  |  |  | 
Before |  |  |  |  |  |  |  |  |  |  |  | 
Physical boundary faces |  |  |  | Partition boundary faces |  |  | Internal faces |  |  |  |  | 
After |  |  |  |  |  |  |  |  |  |  |  | 
4 groups |  |  |  | 3 groups |  |  | 6 groups |  |  |  |  | 
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 18: Design of OpenACC Parallel Regions
Example: face loops after “face renumbering & grouping” | 
The original face loops are nested in a sequential loop over groups. | 
OpenMP version Nfac1 = Njfac do ipass = 1, Npass_ift Nfac0 = Nfac1 + 1 Nfac1 = fpass_ift(ipass) !$omp parallel !$omp do do ifa = Nfac0, Nfac1 do ig = 1, Ngp !... contribution to the face-left element rhsel(:, :, iel) = rhsel(:, :, iel) - flux !... contribution to the face-right element rhsel(:, :, ier) = rhsel(:, :, ier) + flux enddo enddo !$omp end parallel enddo | OpenACC version Nfac1 = Njfac do ipass = 1, Npass_ift Nfac0 = Nfac1 + 1 Nfac1 = fpass_ift(ipass) !$acc parallel !$acc do do ifa = Nfac0, Nfac1 do ig = 1, Ngp !... contribution to the face-left element rhsel(:, :, iel) = rhsel(:, :, iel) - flux !... contribution to the face-right element rhsel(:, :, ier) = rhsel(:, :, ier) + flux enddo enddo !$acc end parallel enddo
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 19: Design of OpenACC Parallel Regions
“Face renumbering & grouping” vs. “element loops”
Advantages No redundant computation. Least intrusion to the original code structures. Recoverable to CPU parallel computing. Disadvantages Sequential groups lead to overheads in initializing more parallel kernels. Remarks No direct comparison of these two strategies is yet conducted for our solver. It is unknown which will render better performance on GPU. 2. Since portability is our design priority, the current approach is a preferred, although optimal performance might be compromised.
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 20: Hardware/Software Resource
CPU
2-way SMPs with AMD Opteron 6128 (Many Core) with 8 cores per socket (16 cores per node) 32 GB DRAM 2.0 GHz core-speed for 6128 Opteron (single core)
GPU
NVIDIA Tesla K20c Memory amount: 5.0 GB Stream processors: 2496
Software (64 bit)
Operating system CentOS 5.7 Linux x86 64 Compilation & runtime suite PGI Accelerator Fortran Compiler (ver. 13.4) OpenMPI (ver. 1.5.5)
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 21: Development of RDGFLO
Workflow for p-multigird Discontinuous Galerkin method
!! Loop over time steps | !! P-multgrid
DO itime = 1, ntime | <ACC> Transfer P1->P0
<ACC> Predict time-step size on higher level | <ACC> Predict time-step size on lower level
!! Loop over TVDRK stages for rDG(P1P2) | <ACC> Compute R.H.S vector R
Do istage = 1, nstage | <ACC> Compute L.H.S matrix A = M/dt – dR/dU
 | <ACC> Solve the linear system Au=R
<ACC> P1P2 lest-squares reconstruction | !! Linear solver + Preconditioner
<ACC> R.H.S. residual from diffusion | ! Preconditioning: P-1Au=P-1R
<ACC> WENO reconstruction | ! Option 1. GMRES + LU-SGS
<ACC> residual from convection | ! Option 2. LU-SGS + Jacobi
<ACC> update solution vector | ! Option 3. Jacobi
 | ! Option 4. …
ENDDO | ENDDO

## Slide 22: Development of OpenACC Parallel Regions
Workflow for implicit rDG method
DO itime = 1, ntime | 
 Predict time-step size | 
 Compute R.H.S vector R | !successfully ported on GPU.
 Compute L.H.S matrix A = M/dt – dR/dU | !successfully ported on GPU.
 Solve the linear system Au=R | 
Jacobi/ LU-SGS/ GMRES algorithm | !Jacobi successfully ported on GPU.
 … | 
 Preconditioning: P-1Au=P-1R | 
Option 0. no preconditioning ✗ | 
Option 1. Jacobi | 
Option 2. LU-SGS | 
ENDDO | 

## Slide 23: Performance Assessment
Timing measurements
Unit running time Tunit where the running time Trun refers to the time recorded for completing the time marching loop with a given iteration number Ntime.
Control sets (simulations in double-precision arithmetic) | 
GPU | Parallel computing with 1 GPU device
CPU | Serial computing with 1 CPU core
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics

## Slide 24: Timing test
Viscous flow over a 3D sphere. M∞ = 0.5, α = 0° and Re=118.
On a set of two tetrahedral grids. (nelem = 62,477 and 200,416) Streamlines plotted on the the computation domain

## Slide 25: Timing test
Timing measurements of using p-multigrid DG methods
 | Tunit by pMG DG(P1) |  |  | Tunit by pMG rDG(P1P2) |  | 
Nelem | GPU | CPU | Speedup | GPU | CPU | Speedup
62,477 | 17.67 | 54.42 | 3.08 | 32.07 | 156.00 | 4.86
200,416 | 16.41 | 54.59 | 3.33 | 30.45 | 162.46 | 5.34

## Slide 26: Timing test
Subsonic flow past a sphere at M∞ = 0.50 and α = 0°.
On a sequence of four successively refined tetrahedral grids. Pressure contours plotted on the surface triangular meshes

## Slide 27: Timing test
Test results on L.H.S.
Timing on L.H.S. |  |  |  |  | 
nelem | 1gpu | 1cpu | speed_up-1 | 16cpu | speed_up-16
535 | 3.00E-03 | 1.20E-02 | 4.00 | 1.23E-04 | 0.04
2426 | 5.45E-02 | 4.27E-01 | 1.16 | 5.36E-03 | 0.10
16467 | 1.35E-01 | 4.27E-01 | 3.16 | 3.78E-02 | 0.28
1247061 | 8.00E-01 | 3.45E+00 | 4.31 | 2.84E-01 | 0.36
Test results on wall-time
Timing on wall-time |  |  |  |  | 
nelem | 1gpu | 1cpu | speed_up-1 | 16cpu | speed_up-16
535 | 9.70E-03 | 3.71E-02 | 3.82 | 3.75E-03 | 0.39
2426 | 6.56E-02 | 1.70E-01 | 2.59 | 1.55E-02 | 0.24
16467 | 1.82E-01 | 1.27E+00 | 6.95 | 1.20E-01 | 0.66
1247061 | 1.15E+00 | 1.14E+01 | 9.93 | 8.10E-01 | 0.71

## Slide 28: Application of RDGFLO
Timing test for Tayler-Green vortex (DNS) on hexahedral and tetrahedral grids ;
Taylor-Green vortex (DNS) with Rosenbrock-Wanner method ;
Implementation of one equation turbulence model in rDG
code.

## Slide 29: Application of RDGFLO – DNS
Explicit rDG periodic boundary condition
Add an array ‘bperi(2,nbfac)’ to store the periodic B.C. information
DNS problem: 3D Taylor-Green vortex problem on hexahedral grid

## Slide 30: Application of RDGFLO – DNS
DNS problem: 3D Taylor-Green vortex problem on hexahedral grid
GPU/CPU computing history of the iso-surface of the z-component of the dimensionless vorticity (nelem =813, 0<t<20s)

## Slide 31: Timing test
Numerical test: Taylor vortex problem on hexahedral grid (DG(P1))
Notes: DGP1 UP TO 15.48(1 v.s.1), 8.85(1 v.s. 16) 3.40 (2 v.s. 32);

## Slide 32: Timing test
Numerical test: Taylor vortex problem on hexahedral grid (rDG(P1P2))
Notes: rDGP1P2 UP TO 13.93 (1 v.s. 1), 1.58 (1 v.s. 16) 3.13 (2 v.s. 32)

## Slide 33: Timing test
Numerical test: Taylor vortex problem on hexahedral grid
Weak Scaling (NVIDIA C2070) |  |  |  |  | 
 |  | Unit Time |  | Parallel Efficiency | 
nelem | nGPU | DGP1 | rDGP1P2 | DGP1 | rDGP1P2
783 (0.5M) | 1 | 15.17 | 21.92 | - | -
1003 (1.0M) | 2 | 15.87 | 23.82 | 95.59% | 92.02%
1263 (2.0M) | 4 | 17.04 | 25.86 | 89.03% | 84.76%
1583 (4.0M) | 8 | 17.13 | - | 88.56% | -

## Slide 34: Application of RDGFLO – DNS
Numerical test: Taylor vortex problem on hexahedral/tetrahedral grid

## Slide 35: Strong Scaling Test (K20c) On Tetrahedral Grids
Test results with DG(P1)
nelem | 1gpu | 1cpu | speed_up-1 | 16cpu | speed_up-16
41,154 | 4.03 | 47.85 | 11.87 | 6.07 | 1.51
511,104 | 3.17 | 47.36 | 14.94 | 4.13 | 1.30
Test results with rDG(P1P2)
nelem | 1gpu | 1cpu | speed_up-1 | 16cpu | speed_up-16
41,154 | 19.68 | 86.13 | 4.38 | 15.92 | 0.97
511,104 | 16.08 | 85.52 | 5.32 | 9.49 | 0.59

## Slide 36: Application of RDGFLO – Rosenbrock-Wanner
Taylor-Green vortex with Rosenbrock-Wanner method
Schemes | dt | Time steps | CPU time
ESDIRK3 | 0.08 | 2500 | 369256.0
ROSI2PW | 0.04 | 5000 | 269021.2
ROS34PRW | 0.04 | 5000 | 255536.2
ROW methods require
27% CPU time less that ESDIRK3.

## Slide 37: Application of RDGFLO – Turbulence model
Sparlart –Allmaras turbulence model for DG (Burgess and Mavriplis)
The variable is designed to remain positive regardless of the value of and is given by
The effect of the modification is to deactivate the production, destruction and diffusion terms of the turbulence model equation when becomes negative.

## Slide 38: Application of RDGFLO – Turbulence model
Test case I.Flat plate with Ma=0.2, Re=500,000, T=300K
The wall-normal spacing: 1.0X10-6
Hexamesh:nelem=13,056 ,npoin=26,578 .
The dimensionless velocity profile
in the boundary layer

## Slide 39: Application of RDGFLO – Turbulence model
Test case II.NACA0012 with Ma=0.15, Re=600,000, T=300K,AoA=10°
The wall-normal spacing : 1.0X10-6
Mesh: Hexahedral
Medium mesh: nelem=14,366 npoin=29,152
Fine mesh : nelem=57,344 npoin=115,648
Ref. solution: Cl = 1.0891-1.10,
Cd = 0.01225-0.01245 .
 | Cl | Cd
Medium | 1.0742676 | 0.01417780
Fine | 1.0848066 | 0.01270036
 | Cl | Cd
Medium | 1.0901676 | 0.01222621
Fine | 1.0884246 | 0.01236461
DG (P1)
rDG (P1P2)

## Slide 40: Application of RDGFLO – Turbulence model
Test case III.Backward Facing Step with Ma=0.128, Re=36,000,T=300K.
The wall-normal spacing : 5.95 X 10-4 ,
Mesh: Hexahedral
 | DG(P1) | rDG(P1P2)
Xr | 6.05 | 6.08
Reattachment location

## Slide 41: Concluding Remarks
Development of RDGFLO
p-Multigrid reconstructed DG method on GPU platform (For viscous ) An average speed-up factor up to 3.3x can be achieved using pMG-DG(P1) An average speed-up factor up to 5.3x can be achieved using pMG-rDG(P1P2) An implicit reconstructed discontinuous Galerkin method on GPU cluster Port R.H.S on GPU platform Port L.H.S on GPU platform Port Jacobi on GPU platform Explicit Periodic Boundary Condition on GPU platform An average speed-up factor up to 13.93x can be achieved using rDG(P1P2) Multiple-GPU computing carries out high parallel efficiency accurate solver for unsteady flow problems
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics
Application of RDGFLO
Taylor-Green vortex (DNS) with Rosenbrock-Wanner method Validating the accuracy and efficiency of Rosenbrock-Wanner method Implementation of one equation turbulence model in rDG code

## Slide 42: Future Work
Development of RDGFLO
p-Multigrid reconstructed discontinuous Galerkin method on GPU platform Renumbering algorithm to avoid memory contention issue for LU-SGS Implicit Rosenbrock method on GPU platform Porting to GPU platform using OpenACC derivatives Fully implicit reconstructed discontinuous Galerkin method on GPU platform Extend the implicit solver onto higher order method to make the fully implicit rDG solver working on GPU platform Attempt to avoid local array issue for GMRES solver
AFOSR BRI – Co-Design of Hardware/Software for Predicting UAV Aerodynamics
Application of RDGFLO
Direct Numerical Simulation for Taylor-Green Vortex problem Extend the current work onto Multi-GPU platform via MPI data transfer to handle finer mesh or problem of larger scale. Turbulent model Port the current explicit turbulent model to GPU platform